## Slide 1: Microwave Controller
Brian lam, Michael Tolmajian, Michael Nava, Sarah Su

## Slide 2: Microwave Controller
Overall Design

## Slide 3: Microwave Controller
Top Simulation

## Slide 4: Buttons
Design Overview

## Slide 5: Buttons
4 total buttons
  Up cycle for power level
  Down cycle for power level
  Start/Stop
  Reset (for entire system)
Edge detector state machine
  Detect only the positive edge of buttons
Each button is debounced
  synched to the clock

## Slide 6: Buttons
Up/Down cycle
  Simple state machine
  Mealy - with button as input and mode bus as output
  Three specific “mode” outputs for the three specific levels
Start/Stop
  Always block constantly checking for button input
  Invert start/idle signals for every button press

## Slide 7: Buttons
DEMO

## Slide 8: LEDs
16 total LEDs
  Used all available LEDs on our Nexys A7 100T FPGA
  Controlled collectively in one array, [15:0]LED
4x16 Decoder
  Each LED lights up using a decoder
  One at a time
Up/Down 4-Bit Counter with a Twist
  16 values, log2(16) = 4 bits (00002 to 11112)
Clock Manager
  32-bit Counter
  32-to-1 Multiplexer

## Slide 10: LEDs
Mode Selecting Module using Case statements (led_modeSelect.v)
  1. Low
    If mode is 2'b01, the 21st bit of the 32-bit counter.
    5 switches for the 32-1 MUX = 5'b10101
    Clock frequency = 108 / 221 Hz
  2. Normal
    If mode is 2'b10, the 20th bit (twice as frequent as Low)
    5 switches for the 32-1 MUX = 5'b10100
    Clock frequency = 108 / 220 Hz
  3. High
    If mode is 2'b11, the 19th bit (twice as frequent as Normal, four times more frequent than Low)
    5 switches for the 32-1 MUX = 5'b10011
    Clock frequency = 108 / 219 Hz

## Slide 11: LEDs
Up/Down 4-Bit Counter (UDAltCounter.v)
  The switch for U/D is controlled by the module.
    It alternates. Hence, UDAltCounter.
  U/D is initially set to 0 (counting up to 15, right to left on LED set).
  When the count is 15, U/D is set to 1 (counting down to 0, left to right on LED set).
U/D Counter and 4x16 Decoder utilized in a testbench; U/D alternates.

## Slide 12: LEDs
DEMO

## Slide 13: Switches
12 total switches
  Sets time for countdown
  6 for minutes
  6 for seconds
  Binary representation

## Slide 14: Switches
Minute-Second Down Counter
  Decrements minutes every minute
  Decrements seconds every second (when seconds reaches 0, next value will be 59)
  Starts counting from the time indicated by the switches after the Start/Stop button is pressed
  Start/Stop button pauses/resumes the counting
  Stops counting when minutes = 0 and seconds = 0
  Resets to initial switch values when Reset button is pressed
Digit Separator
  Separates the minutes and seconds into 2 digits using division and modulus operator

## Slide 15: Switches Design Overview

## Slide 16: 7 Segment Display
6 total 7 Segment Displays
  2 used to display the mode
  4 used to display the timer (2 digits for minutes and 2 digits for seconds)
Clock Divider
  Produces a 1 Hz and 400 Hz clock signals
  1 Hz clock is used in the minute-second down counter
  400 Hz clock is used in the anode controller to control the refresh rate of the 7 Segments

## Slide 17: 7 Segment Display
2 total 7 Segment Displays to display the mode
  If mode is 2'b01, the digits will display 'L o'
  If mode is 2'b10, the digits will display '- -'
  If mode is 2'b11, the digits will display 'H i'
4 total 7 Segment Displays to display the timer
  Display the minutes and seconds in BCD

## Slide 18: Display patterns for timer

## Slide 19: 7 Segment Display
Display patterns for modes

## Slide 20: 7 Segment Display Design Overview

## Slide 21: VGA
Three modules total
  Horizontal counter
  Vertical counter
  Top module
Horizontal counter
  Simple up-counter
  0 – 799
  25.1MHz clock
  Enable signal output for Vertical counter every cycle
Vertical counter
  Simple up-counter
  0 – 524
  25.1MHz clock
  Enable signal input from Horizontal counter

## Slide 22: VGA
Top module
  Instantiate Horizontal and Vertical counter
  3-bit RGB registers to control color within always block
    Assigns RGB output values when counters in addressable video time
  25.1MHz clock sensitive always block
25MHz clock sensitive always block
  Lots of if else if statements to control VGA design output
  Calculated values of horizontal and vertical counters to design microwave image chunks at a time

## Slide 23: VGA
PICTURES
IDLE
ON

## Slide 24: UART
Baud rate generator
  9600 bits per second
  Uses timer ticks to read value about halfway into each data bit
Transmitter
  Takes 8 serial inputs one bit at a time and outputs 8 bits in parallel
Receiver
  Takes 8 serial inputs one bit at a time and outputs 8 bits in parallel
FIFO (first in, first out)
  Stores each 8-bit value until ready to be used

## Slide 25: UART
Only receiver is necessary for this project
  Serial communication only from PC to board through microUSB port
  Keyboard inputs will be received by the FPGA board
Receiver pulse signal
  Receiver module outputs one clock cycle pulse when 8 bits have been processed
  Pulse will trigger start/stop mechanism like a button

## Slide 26: Thank You!